## Slide 1: PV Converter Board
Receiver Unit Testing Results,
Updated Design Calculations and Schematics

## Slide 2: Receiver Unit Testing

## Slide 4
Series Arrangement,
4-PV Cells,
Form Factor 2
(Unit Testing without DC-DC Converter using the Electrical Load Instrumentation)

## Slide 5: Receiver Unit Testing Measurements
Input Laser Optical Power = 10 W
Voc = 9.98 V
Iactual = 0.007 A
Output Electrical Power = (9.98 V)(0.007 A) = 0.06986 W
Isc = Imax = 9.8 mA at Vout = 0 (Set)
The system demonstrates power loss based on the expected output power = 0.421024 W.

## Slide 6
Solar Cell: Si-based vertical multi-junction PV cell
Solar Cell
ESP32 Wi-Fi Camera
DC-DC Converter
PC Computer
Wi-Fi Video Stream
Heat Sink
Operating Temperature: 25
Plated Temperature Sensor
TEG (Thermoelectric Generator)
Pconverted
Vout = 5 V
Heatdiss
Receiver Conceptual Block Diagram
Preliminary Receiver System
Conceptual Block Diagram
TEC (Thermoelectric Cooler)
8 V < Vin < 30 V

## Slide 7
New Receiver Load: RSL20 Camera

## Slide 8
New Receiver Load: RSL20 Camera

## Slide 9
CONNECTING THE RECHARGEABLE BATTERY:
• BAT type: Li or Li−Po
• BAT voltage = 3.7 V
• BAT floating voltage = 4.2 V
• Capacity = based on the use case
(recommended 1700 mAh)
The charging current of the FAN54120 is fixed on the
board to 400 mA (fast charge). The following description
and tests relate to Li−Po battery type LP435656:
3.7 V 1700 mAh fitting into the PCB design dimensions.
Emulating The Rechargeable Battery Unit with the PV Power Converter Circuit

## Slide 10
CONNECTING THE PV POWER CONVERTER “CHARGER”
TO POWER THE RSL20 CAMERA LOAD:
• Emulated BAT wattage = 3.7 V x 1700 mAh = 6.29 W
• Emulated BAT floating wattage = 4.2 V x 1700 mAh = 7.14 W
The charging current of the FAN54120 Charger IC is fixed on the
board to 400 mA (fast charge):
• Emulated BAT fast charge wattage = 3.7 V x 400 mA = 1.48 W

## Slide 11
Circuit Design # | PV Cell Arrangement Type | Number of PV Cells | PV Cell Form Factor | DC-DC Converter Type | Output Voltage | Output Current | Output Power
1 | Series | 4 | 1 cm x 1 cm (10 mm x 10 mm) | Boost | 29.21 V x 4 PV cells = 116.84 V | 0.02029 A | 2.3706836 W
2 | Isolated | 1 | 1 cm x 1 cm (10 mm x 10 mm) | Boost | 29.21 V x 1 PV cell = 29.21 V | 0.02029 A | 0.5926709 W
3 | Parallel | 4 | 1 cm x 1 cm (10 mm x 10 mm) | Boost | 29.21 V | 0.02029 A x 4 PV cells = 0.08116 A | 2.3706836 W
4 | Parallel | 4 | 2.5 cm x 2.5 cm (25 mm x 25 mm) | Boost | 2.23 V | 0.0472 A at Pmpp | 0.105256 W
5 | Series | 4 | 2.5 cm x 2.5 cm (25 mm x 25 mm) | Boost | 2.23 V x 4 PV cells = 8.92 V | 0.0472 A at Pmpp | 0.421024 W
6 | Parallel | 4 | 2.5 cm x 2.5 cm (25 mm x 25 mm) | Boost | 2.23 V | 0.0472 A at Pmpp | 0.105256 W
7 | Series | 4 | 5 cm x 5 cm (50 mm x 50 mm) | Boost | 2.43 V x 4 PV cells = 9.72 V | 0.14 A | 1.3608 W
8 | Parallel | 4 | 5 cm x 5 cm (50 mm x 50 mm) | Boost | 2.23 V | 0.14 A x 4 PV cells = 0.56 A | 1.2488 W

## Slide 12: 1. Design Specifications 1 cm x 1 cm MIH® VMJ PV Cell Form Factor, 4-PV, Series
Peripherals:
  Inputs:
    PV Array: 2 leads (+ and -) x 4 PV cells = 8 leads
    TEG module’s 2 leads (+ and -)
    TEC module’s 2 leads (+ and -)
  Outputs:
    ESP-32 Wi-Fi camera
Internals:
  Pads for soldered PV cells
  I/O Ports as Female Connectors
Voltage Requirements:
  Input:
    Each PV cell has a 0.02029 A maximum current output
    Each PV cell has a 29.21 V maximum voltage output
    Each PV cell has a 0.59267 W maximum power output
    Total max Vout = 29.21 V x 4 PV cells; Voltage output = 116.84 V for a series connection
    Total max current = 0.02029 A for a series connection
  Output: 5 V at 180 mA *or .18 A = 0.9 W
Miscellaneous:
  Heat Sink
*Required Separately: Buck DC-DC Converter circuit: 116.84 V to 5 V
PV 1
PV 2
PV 3
PV 4

## Slide 13
Heat Sink
Operating Temperature: 25
Updated Receiver System
Conceptual Block Diagram
RSL20 Camera
PV 2
PV 3
PV 4
+
+
+
+
-
-
-
-
-
-
-
-
+
+
+
+
PV 1
Boost DC-DC Converter

## Slide 14: 5. Design Specifications, 2.5 cm x 2.5 cm PV Cell Form Factor, 4-PV, Series
Peripherals:
  Inputs:
    PV Array: 2 leads (+ and -) leads
    TEG module’s 2 leads (+ and -)
    TEC module’s 2 leads (+ and -)
  Outputs:
    ESP-32 Wi-Fi camera
Internals:
  Pads for soldered PV cells
  PWM Control DSP, MCU, or FPGA for Switch Control
  Buck DC-DC Converter circuit with Low-Pass Filter: 8.92 V to 5 V
  - R, L, C, MOSFET Switch (Voltage-Controlled)
  I/O Ports as Female Connectors
Voltage Requirements:
  Input: 8 - 30 V:
    Each PV cell has a 0.1053 W maximum power output
    Each PV cell has a 2.23 V voltage output at Pmpp
    Total Vout = 2.23 V x 4 PV cells; Voltage output = 8.92 V for a series connection
    Total current = 0.0472 A current output at Pmpp for a series connection
  Output: 5 V at 180 mA or 0.18 A = 0.9 W
Miscellaneous:
  Heat Sink
PV 1
PV 2
PV 3
PV 4

## Slide 15
Heat Sink
Operating Temperature: 25
Updated Receiver System
Conceptual Block Diagram
RSL20 Camera
PV 2
PV 3
PV 4
+
+
+
+
-
-
-
-
-
-
-
-
+
+
+
+
PV 1
Boost DC-DC Converter

## Slide 16: 7. Design Specifications, 5 cm x 5 cm PV Cell Form Factor, 4-PV, Series
Peripherals:
  Inputs:
    PV Array: 2 leads (+ and -) leads
    TEG module’s 2 leads (+ and -)
    TEC
  Outputs:
    ESP-32 Wi-Fi camera
Internals:
  Pads for soldered PV cells
  PWM Control DSP, MCU, or FPGA for Switch Control
  Buck DC-DC Converter circuit with Low-Pass Filter: 9.72 V to 5 V
  - R, L, C, MOSFET Switch (Voltage-Controlled)
  I/O Ports as Female Connectors
Voltage Requirements:
  Input: 8 - 30 V:
    Each PV cell has a 0.34 W power output
    Each PV cell has a 2.43 V voltage output
    Total Vout = 2.43 V x 4 PV cells; Voltage output = 9.72 V for a series connection
    Total current = 0.14 A for a series connection
  Output: 5 V at 180 mA or 0.18 A = 0.9 W
Miscellaneous:
  Heat Sink
PV 1
PV 2
PV 3
PV 4

## Slide 17
Heat Sink
Operating Temperature: 25
Updated Receiver System
Conceptual Block Diagram
RSL20 Camera
PV 2
PV 3
PV 4
+
+
+
+
-
-
-
-
-
-
-
-
+
+
+
+
PV 1
Boost DC-DC Converter